## Slide 1: The Effect of Effluent Pipe Discharge on Dry Run Creek
Benny Harken & Michael Stebbins

## Slide 2: Goals
For our project we wanted to see how effluent pipes discharge effects the water quality of Dry Run Creek.

## Slide 3: Methods
We chose 3 different sites
  ROTH
  University Ave
  Towers
At each site we sampled 3 different sets of water
  Above
  Effluent
  Below

## Slide 4: Methods
We sampled 6 different parameters
  pH
  Total dissolved solids
  Conductivity
  Temperature
  Dissolved oxygen
  Turbidity

## Slide 5: ROTH
Our first location that we took samples from is located near the footbridge going across Dry Run Creek near the Well Monitoring Station
The effluent pipe runs from Married Student Housing into the creek

## Slide 9
Chart: ROTH pH
| Above | Effluent | Below
20-Oct | 8.36 | 8.36 | 8.44
24-Oct | 8.31 | 8.3 | 8.29
27-Oct | 8.39 | 8.32 | 8.34
2-Nov | 8.34 | 8.36 | 8.35
3-Nov | 8.27 | 8.32 | 8.31
10-Nov | 8.22 | 8.46 | 8.27

## Slide 10
Chart: ROTH TDS
| Above | Effluent | Below
20-Oct | 409 | 914 | 405
24-Oct | 387 | 986 | 413
27-Oct | 418 | 975 | 508
2-Nov | 300 | 153 | 112
3-Nov | 380 | 690 | 433
10-Nov | 367 | 630 | 380

## Slide 11
Chart: ROTH Conductivity
| Above | Effluent | Below
20-Oct | 589 | 1313 | 587
24-Oct | 560 | 1423 | 632
27-Oct | 604 | 1414 | 737
2-Nov | 435 | 223 | 163
3-Nov | 552 | 996 | 628
10-Nov | 530 | 915 | 551

## Slide 12
Chart: ROTH Temperature
| Above | Effluent | Below
20-Oct | 9.2 | 10.3 | 10
24-Oct | 14.6 | 17.7 | 15.3
27-Oct | 13 | 12.1 | 10.7
2-Nov | 11.4 | 8.6 | 9.6
3-Nov | 13.3 | 12.4 | 9.8
10-Nov | 8.5 | 14.2 | 6.1

## Slide 13
Chart: ROTH Dissolved Oxygen
| Above | Effluent | Below
20-Oct | 11.93 | 10.59 | 11.18
24-Oct | 10.84 | 8.6 | 10.38
27-Oct | 11.46 | 9.17 | 11.04
2-Nov | 9.36 | 10.38 | 10.39
3-Nov | 10.75 | 9.64 | 10.77
10-Nov | 10.73 | 9.89 | 11.16

## Slide 14
Chart: ROTH Turbidity
| Above | Effluent | Below
20-Oct | 2.66 | 0.4 | 4.16
24-Oct | 5.15 | 1.15 | 2.33
27-Oct | 12.2 | 9.62 | 6.21
2-Nov | 46.3 | 46.9 | 37.7
3-Nov | 9.27 | 13.7 | 4.64
10-Nov | 12.9 | 8.7 | 23

## Slide 15: Results
Total dissolved solids and conductivity are directly related
Effluent had slight effect on pH, TDS, and Conductivity

## Slide 16: University Avenue Bike Trail
Our second location is located under University Ave. right next to the Bike trail that runs under it which is located next to the Cedar Falls Lutheran Home
The effluent pipe is located on the East side of the creek under the bridge

## Slide 20
Chart: University Ave pH
| Above | Effluent | Below
20-Oct | 8.23 | 8.31 | 8.2
24-Oct | 8.23 | 8.16 | 8.23
27-Oct | 8.15 | 8.27 | 8.27
2-Nov | 8.12 | 8.2 | 8.18
3-Nov | 8.27 | 8.09 | 8.26
10-Nov | 8.32 | 8.25 | 8.29

## Slide 21
Chart: University Ave TDS
| Above | Effluent | Below
20-Oct | 434 | 503 | 440
24-Oct | 417 | 445 | 416
27-Oct | 445 | 493 | 446
2-Nov | 385 | 76 | 214
3-Nov | 367 | 482 | 391
10-Nov | 371 | 462 | 375

## Slide 22
Chart: University Ave Conductivity
| Above | Effluent | Below
20-Oct | 628 | 726 | 637
24-Oct | 602 | 643 | 603
27-Oct | 646 | 715 | 647
2-Nov | 562 | 114 | 311
3-Nov | 541 | 712 | 559
10-Nov | 543 | 676 | 544

## Slide 23
Chart: University Ave Temperature
| Above | Effluent | Below
20-Oct | 10 | 10.8 | 9.9
24-Oct | 15.3 | 16.8 | 14.9
27-Oct | 12.6 | 13.6 | 12.2
2-Nov | 8 | 7.7 | 8.2
3-Nov | 9.1 | 13.3 | 8.6
10-Nov | 6.1 | 11.7 | 5.9

## Slide 24
Chart: University Ave Dissolved Oxygen
| Above | Effluent | Below
20-Oct | 10.96 | 9.95 | 10.7
24-Oct | 10.36 | 9.15 | 10.35
27-Oct | 10.22 | 9.24 | 10.46
2-Nov | 9.37 | 11 | 10.62
3-Nov | 10.99 | 9.67 | 10.87
10-Nov | 11.31 | 9.35 | 11.47

## Slide 25
Chart: University Ave Turbidity
| Above | Effluent | Below
20-Oct | 0.69 | 0 | 0.51
24-Oct | 3.35 | 0.05 | 5.17
27-Oct | 6.35 | 4.27 | 4.4
2-Nov | 27.3 | 51.1 | 34.5
3-Nov | 0.54 | 1.06 | 5.67
10-Nov | 3.14 | 0.53 | 5.22

## Slide 26: Results
Total dissolved solids and conductivity are directly related
Effluent appeared to have virtually no effect on the stream

## Slide 27: Towers Location
Our third location is located near Dancer and Rider under Campus Street
The effluent pipe is located under the bridge that crosses Dry Run Creek

## Slide 30
Chart: Towers pH
| Above | Effluent | Below
20-Oct | 8.43 | 8.35 | 8.38
24-Oct | 8.42 | 7.99 | 8.01
27-Oct | 8.38 | 8.18 | 8.19
2-Nov | 8.31 | 8.23 | 8.12
3-Nov | 8.34 | 8.38 | 8.37
10-Nov | 8.38 | 8.36 | 8.39

## Slide 31
Chart: Towers TDS
| Above | Effluent | Below
20-Oct | 332 | 304 | 318
24-Oct | 400 | 385 | 387
27-Oct | 394 | 400 | 391
2-Nov | 137 | 57 | 126
3-Nov | 334 | 338 | 742
10-Nov | 338 | 766 | 345

## Slide 32
Chart: Towers Conductivity
| Above | Effluent | Below
20-Oct | 465 | 451 | 460
24-Oct | 579 | 560 | 562
27-Oct | 575 | 587 | 565
2-Nov | 199 | 86 | 187
3-Nov | 484 | 548 | 1075
10-Nov | 490 | 1130 | 492

## Slide 33
Chart: Towers Temperature
| Above | Effluent | Below
20-Oct | 10.8 | 11 | 10.3
24-Oct | 13.3 | 15.6 | 14.4
27-Oct | 13 | 14 | 16.6
2-Nov | 6.7 | 7.2 | 7.2
3-Nov | 8.34 | 8.38 | 10
10-Nov | 5.2 | 8.7 | 6.6

## Slide 34
Chart: Towers Dissolved Oxygen
| Above | Effluent | Below
20-Oct | 11 | 10.78 | 11.67
24-Oct | 12.3 | 9.49 | 9.82
27-Oct | 11.86 | 10.16 | 9.77
2-Nov | 11.28 | 11.87 | 11.2
3-Nov | 11.75 | 11.39 | 10.4
10-Nov | 12.49 | 10.45 | 11.24

## Slide 35
Chart: Towers Turbidity
| Above | Effluent | Below
20-Oct | 2.49 | 0.77 | 2.11
24-Oct | 4.6 | 0.12 | 1.55
27-Oct | 14.7 | 1.68 | 0.68
2-Nov | 37.2 | 24.7 | 55.7
3-Nov | 6.5 | 1.23 | 3.47
10-Nov | 5.73 | 2.21 | 4.85

## Slide 36: Results
Total dissolved solids and conductivity are directly related
Effluent had more significant effect on pH, temperature, and turbidity
Little effect was noticed for DO, conductivity, and TDS

## Slide 37: Conclusion
Towers site had largest effect on stream
  Largest volume of effluent water
Overall there was no large effect for the parameters we sampled
Temperature differences could have been due to shaded vs non shaded areas of the stream
Rain greatly reduces the conductivity and total dissolved solids while increasing turbidity
Snow had no effect

## Slide 38: Questions?